FC-1325MA配置单

适用范围:

广泛应用于家具加工行业、家装业、木工装饰业、门业、木制工艺品金属制品，石材等行业的加工制作。

机型特点：

- 床身采用优质钢结构焊接而成,经过二次淬火处理，稳定性较高。

- 配备大功率步进驱动电机，X、Y、Z轴均采用进口直线运动导轨，运行平稳，免维护，使用寿命高。

- 采用高精齿轮齿条传动,最高运行速度可达30M/MIN,雕刻1MM小字清晰分明。

- 主轴电机采用意大利HSD风冷主轴,每分钟18000转,适合于木制品行业长时间加工。

- 超强吸力真空装置，内置负压储气设备 400立升大流量真空泵，使工件定位牢固，快捷。

- 先进的专业控制系统兼容多种指令格式，可实现断电、断点、隔天加工功能，更方便省力。

- 备注：本机型可选配伺服控制系统，整机性能加工效率可提高50%。

FC-1325MA性能参数

| 外形尺寸 | 1850*3000*1600mm |
| --- | --- |
| X、Y轴工作行程 | 1300*2500mm |
| Z轴行程 | >220mm |
| 平台尺寸 | 1340*2500mm |
| 最大运行速度 | 30m/min |
| 最大进料高度 | 220mm |
| 分辨率 | 0.025mm |
| 雕刻指令 | G代码、uoo.mmg.plt |
| 软件运行环境 | Windows98/2000/xp |
| 功率（不含主轴） | 2KW |
| 工作电压 | AC380V/50HZ |
| 主轴功率 | 6.0KW（HSD）/4.5KW(国产可选) |
| 主轴转速 | 6000-18000rpm/min |
| 工作方式 | 步进（齿条传动） |

联系人：吴霖                              北京珂明伟业科技发展有限公司

电话：010-60277122手机15001016657           传真：010-60273123

网址：www.kemingchina.com              E-mail：kemingchina0125@126.com

地址：北京市丰台区南三环中路70号南曦大厦D座801    邮编：102609

工厂地址：北京市通州区张家湾镇里二泗工业园124号

FC-1325MA

Scope of application:

Widely used in furniture processing industry， upholstery, decorative woodwork, doors, woody handicrafts and metal product and stone product.

Features of the machine:

- The lathe welded use high-quality steel,by secondary quenching processing that ensures the high stability.

- Equip large power stepping drive motor;X,Y,Z axises chosen imported straight moving rails,smoothly running,without maintainion,long used.

- Using high accurate pinion and rack transmission. The highest speed is 30m/min. It can clearly engrave the 1mm small word.

- Spindle use Italy HSD water-cold spindle,18000rot/min,fit for long time producing in the woodwork line

- Overstrong suction vacuum fittings,install negative pressure reservoir equipment，400L large space vacuum pump, the parts orientate fastness,swift.

- Advanced industrial controlling system is compatible to many dictate formats that can operate after accident or next day processing so it is very convenient.

- Remark:This machine can fit for servo system that make efficiency increase 50%.

FC-1325MA Performance parameter:

| Outer dimension | 1850*3000*1600mm |
| --- | --- |
| X,Y axis travel | 1300*2500mm |
| Z axis travel | ＞220mm |
| Table area | 1340*2500mm |
| Max running speed | 30m/min |
| Max engraving speed | 15m/min |
| Max feed-in height | 220mm |
| Command language | G code, M code |
| Software operating environment | Windows98/2000/xp |
| Power (not include spindle) | 2kw |
| Work voltage | 380v/50Hz |
| Spindle power | 6.0kw(HSD)/4.5KW(domestic for chosen) |
| Spindle rotating speed | 6000-18000rpm/min |
| Work mode | Stepping(rack transmission) |