SF-02

Deck Mounted Single Hole Faucet-DC

PRODUCT TYPE

Deck mounted single hole faucet

FEATURES & SPECIFICATIONS

·Polished chrome plated finish

·Solid brass internal waterway construction

·Efficient dual beam infrared sensors

·5 GPM (1.9 L/min) vandal resistant spray outlet

·Inlet supply check valves

·Multiple field adjustable modes and ranges

·4 AA batteries as power supply

·Low battery indicator

·Above deck hermetically sealed electronics

·Above deck water-tight solenoid with filter screen

·Mounting hardware included

OPTIONAL ACCESSORIES

·Copper inlet tube

·Thermostatic mixing valve

·Includes optional 2.2 GPM (8.3 L/min) pressure

compensating aerator insert

PERFORMANCE SPECIFICATION

·Rated Operating Pressure: 20-125 PSI

·Rated Operating Temperature: 40-140° F

·3-Year Battery Life or Approximately 200,000 Uses

WARRANTY

·5-Year Limited Mechanicals Warranty

·3-Year Limited Electronics and Solenoid Warranty

·1-Year Limited Finish Warranty

COMPLIANT TO

·CCC

Yotun Electronic Co. Ltd. offers sanitation hardware for schools, laboratories, hospitals, office buildings, food service, airports and sport facilities.

PHOTOS