产品规格书

A、产品图示：

IP1350S

B、产品明细：

- 产品名称：太阳能充电器

- 产品型号：IP1350S

- 适用类别：数码产品适用型

- 电池类型：聚合物锂电池

- 电池容量：1350mAH

- 输出电压：5.5V  /  700mA

- 最大电流：1800mA

- 太阳能板：50*55*1.5mm

- 太阳能功率：5.5V ; 35mA

- 单机重量：45g

- 产品毛重：0.06KG

- 产品尺寸：14.5x55.7x60.8 mm

- 配件1：充电输入线：1条；

- 配件2：

- 包装方式：中性PVC/卡纸包装 （可指定OEM）

- 外箱尺寸：61*33.5*46.5 （可指定OEM）

- 装箱数量：100台/箱    （可指定OEM）

备注：

1、产品颜色可选，目前有黑色、白色；

2、太阳能板转换效率15%以上；

C、产品特点：

1、适用应急场合：在野外作业或旅游，或停电时，太阳能充电宝会帮您很大的忙，确保信息时代永不间断。

2、使用方便  ： 无论何时何地，您都可以极为方便的给您的手机充电或其它数码产品充电。

3、高效率充电：给您的手机充电60分钟，可以获得120-150分钟通话时间或者72小时待机时间。

4、环保，节约能源： 使用绿色能源太阳能，可为环保作出您的贡献。

5、外形时尚，携带方便  造型简洁华贵，小巧玲珑，携带方便。

6、使用安全：带有充电过充保护，有效延长您的手机电池的使用寿命，使用安全

7、太阳能持续充电让充电器始终保持荷电状态，太阳能充电10~15小时，可增加充电器足够有效电量进行应急充电。

8、用电脑或交流适配器给充电器内置电池充电时间：2-3个小时

9、如因短路保护，仅需拔掉短路负载， 10秒钟既可恢复供电。

本产品适用于下列产品充电*

手机（标准配置有诺基亚，三星，苹果，摩托罗拉，索爱，迷你电器、）*数码相机*PDA*MP3

*MP4（内置可充电电池容量须小于1350mAh

How to Charge your power station:

1)put your power station under sunlight to charge.

2)connect your power station to jack via the AC adapter to charge

3)connect your power station to your PC via the USB cable attached

universal solar charger

compatible with:

*iphnoe/ipod series

*ALL kinds of brand cell phones

*All kinds of MP3.MP4 players

*All kinds of digital camera