承   认   书

Specification For Approval

| 产 品 名 称 | Φ12×9.5电磁有源蜂鸣器 |
| --- | --- |
| PRODUCT NAME |  |
| 鑫 亚 图 产 品 型 号 | AT12095V5A |
| A&T PART NUMBER |  |
| 客户型号 / 客户名称 | 纬达信 |
| Customer’s Model No/Customer’s Name |  |

客户确认：（签署和签章） Approved By:(Signature and Chop)

日期Date: 年YY 月MM 日DD

| 批 准 Approved By | 审 核 Checked By | 拟 制 Drafted by |
| --- | --- | --- |

# PIEZOELECTRO TRANSDUCER SPECIFICATION

| Customer:纬达信 | Part No: |
| --- | --- |
| Product: Magnetic Buzzers | A&T Part No：AT12095V5A |
| Technical Terms |
| Resonant Frequency (KHZ) | 2.4±0.5 |
| Rated Voltage (VDC) | 5.0 |
| Operating Voltage (VDC) | 3.0~7.0 |
| Max. Current Consumption at Rated Voltage (mA) | 35 |
| Min. Sound Output at 10cm at Rated Voltage (dB) | 80 |
| Operating Temperature (0C) | -20~+70 |
| Storage Temperature (0C) | -30~+80 |
| Environmental Protection Regulation | RoHS |
| Buzzer Soldering process | Soldering Parameter |
|  | Temp.( 0C) | Time(Sec.) | Times |
| Inclusive Lead |  | Reflow soldering | 230±10 | above 1700C time 40~70 | 2 |
|  |  | Wave soldering | 245±5 | 3~6 | 1~2 |
|  |  | Manual soldering | 330±10 | 1~2 | 1~2 |
| Lead Free |  | Reflow soldering | 245±15 | above 1800C time 40~70 | 3 |
|  | ★ | Wave soldering | 260±5 | 4~8 | 2~3 |
|  | ★ | Manual soldering | 350±10 | 1~3 | 2~3 |

Remark: ★A&T Instance Soldering Process

APPEARANCE DRAWING    Tol : ± 0.5  Unit: mm

# Text boxes

File Code : RDYP091116105

Rve:  0