| 技术参数/型号 Technical information/mode | TY-0604A | TY-0609A | TY-0912A | TY-1215A | TY-1218A |
| --- | --- | --- | --- | --- | --- |
| 外形尺寸 Overall dimension | 98*53*92cm | 128*93*92cm | 158*133*92cm | 185*161*92cm | 215*135*92cm |
| 切割面积 Cutting area | 610*410mm | 920*610mm | 1220*920mm | 1500*1200mm | 1800*920mm |
| 工作特性 Operation properties | 电脑操作与切割同时进行，快速完成数据传输，可连续使用 Computer operation and cutting machines can be used simultaneously for quick data transmission capable of continuous operations |
| 切割速度 Cutting speed | 最快1200mm/min 1200mm/min quickest |
| 切割厚度 Cutting thickness | <2mm |
| 切割材料 Cutting materials | 布料、皮革、毛料、黄厚纸板、红硬纸板、PVC板、白卡纸、鸡皮纸、纤维中底板以及塑胶板等 Yellow thick paper board, red hard paper board, PVC board, ivory cardboard, sulphite paper,insole fiberboard and plastic board, etc |
| 切割方式 Cutting style | 多用途刀座，N组不同的笔画、半刀、全刀设置 Multipurpose blade holder, N groups of different strokes, half blades |
| 笔型/刀型 Pen shape/cutter shape | 普通的签字笔、油性笔、圆珠笔/特种进口钨钢刀 Common gel pens, oily pens, ball pens/specific tungsten steel cutter |
| 固定方式 Fixing manner | 双面胶粘贴/真空吸附/静电吸附 Double-sided adhesive/vacuum absorption/static absorption |
| 机械分辨率 Mechanical resolution | 0.007mm |
| 软件分辨率 Software resolution | 0.025mm、0.01mm、0.1mm可选 0.025mm, 0.01mm, 0.1mm optional |
| 传输接口 Transmission interface | 标准并口、串口、USB Standard parallel port and serial port |
| 数控面板 Digital control panel | 手持控制器及液晶显示触控屏 |
| 传动材料 Transmission materials | 日本进口直线导轨 Imported straight-line guide rail |
| 工作电压/功率 Supply voltage/power | 交流220V ± 10%/50Hz AC 220V ± 10%/50Hz |
| 保险丝规格 Fuse specification | 10A 10A |
| 电机 Servomotor | 步进电机、伺服电机 Step motor, servomotor |

鸿佰成电脑样板绘图切割机

HongBaiCheng Computer Sample Plotters and Cutting Machines

保修1年

Warranty for 1 Years

＊      控制系统采用美国嵌入式上位机系统

＊      Flushbonading upper monitor in control system

＊      传动系统全面采用进口直线导轨，速度快，精度高，声音小，质量稳定。

＊      Imported straight-line guide rails are used for the transmission system at a quick speed, high accuracy, low noise and steady quality.

＊      电机采用日本进口原装件，其他传动件也多数采用进口部件。

＊      Montor was imported from Japan, most other driving medium are also imported.

＊      切割速度达0-1200mm/min。

＊      cutting speed is at 1200mm/min.

＊      标准I/O接口，控制器使用USB2.0高速接口进行数据通讯,数据传输高效安全,可连接任意CAD软件.

＊      Standard I/O interface, controller use USB2.0 high speed interface to transport datea, it’s high security, can connected to any CAD software.

＊      适用行业:服装、制鞋、箱包手袋、布制玩具、激光刀模绘图、灯饰、广告礼品、不干胶、彩盒包装等行业之绘图与切割的专业型客户

Appliable industry: clothing, shoemaking, bag/handbags,fabric toy, lasre mould drawing, lighting, advertising gift,pressure-sensitive adhesive.

适用材料：布料、皮革、毛料、黄厚纸板、红硬纸板、PVC板、白卡纸、鸡皮纸、纤维中底板以及塑胶板等

Appliable material:fabric. Leather, wollens, yellow thick paper board, read hard paper board,PVC, Ivory board, M.G. wrapping paper,fiber baseboard, plastic board.