对数周期天线（11）

Logarithm Cycle Antenna

| Model | TDJ-800/2500-11 |
| --- | --- |
| Electrical Specifications |
| Frequency Range 800-960/1710-2500MHZ VSWR ≤1.4 Input Impedance 50Ω Gain 11/12dBi Polarization Vertical Horizontal Beamwidth 65°/ 50° Vertical Beamwidth 50°/ 40° Front to Back Ratio ≥25dB Max,power 200W First Below Null-Fill ＜21dB Connector Type N Female Intermediation IM3 ≤-107dBm Lightning Protection DC ground |
| Mechanical Specifications |
| Dimension 300×210×65mm Weight 1.1kg Working temperature -40℃~+70℃ Radome material UV Protected ABS |
| 型 号 | TDJ-800/2500-11 |
| 电 性 能 指 标 |
| 频率范围 800-960/1710-2500MHZ 电压驻波比 ≤1.4 输入阻抗 50Ω 增益 11/12dBi 极化形式 垂直极化 水平波瓣宽度 65°/ 50° 垂直波瓣宽度 50°/ 40° 前后比 ≥25dB 最大功率 200W 波瓣电平 ＜21dB 接口形式 N型阴头 三阶互调 ≤-107dBm 闪电保护 直流接地 |
| 机 械 指 标 |
| 尺寸 300×210×65mm 重量 1.1kg 工作温度 -40℃~+70℃ 天线罩材料 防紫外线ABS |

说 明 书                 SPECIFICATION