FQ-1520A 分切复卷机
    Cutting rewinder machine
    设备用途：用于各种成卷薄膜材料的裁断加工。适用于pvc.pp.热转印膜、油漆纸等材料。宽度自由调节，裁断尺寸精确。并且采用多轴多刀设计，可以多个尺寸同时进行同时进行裁切。使用其中轴，可裁切很小的尺寸。使用变频器或电磁调速控制裁切速度。
    Function:
    This machine can be used to cut up pvc.pp.hot transfer film.melamine paper and other roll membrance materials,you can regulate the wide freely and can obtain the percise size .It can cut in different sizes at one time .add the air-expanded reel so it can cut up in a small size ,The cutting speed is monitored by transducer or electrical magnetism timing engine.
    技术参数(Technical Specifications)：
    最大裁切宽度（Maximum width of the cutting piece ）： 1350mm
    最小裁切宽度（Minimum diameter of cutting piece ）： 25mm
    最大膜卷直径（Maximum diameter of rolling piece ） 400mm
    标准切刀数量（amount of the standard cutting piece ） 6把
    最大切刀数量（Maximum amout of the cutting piece ） 20把
    裁切速度（cutting Speed）: 20-80m/min
    电机功率（power）:1.5kw
    压缩空气（compressed air） 6kg/c㎡
    外行尺寸（Exterior size）2200mm×900mm×1250mm

济南利鸿机械有限公司位于济南的东部地区，是一个年轻的有生命力的企业，本着高品质、高效率、高技术的工作原则在木工机械行业中努力的拼搏。诚信是公司的基本工作方针。 本公司主要生产木工机械（覆膜机、板材包覆机、分切机、正负异形压机等）但从技术创新方面考虑，又增加了一套流程，已达到自给自足、自主创新的目的。可以全方面满足客户需求，可谓用户最理想的生产商！ 我们公司不同于一般的企业实体，我们最大的优势在于创新，科技是公司发展的最主要动力。