ELECTRIC BEVELER

■The quick and convenient solution for adding bevels and deburring. ■Excellent for following curved shapes. ■Variable speed for working with a variety of materials. ■Uses standard triangle carbide inserts. ■Quick and easy tool-free bevel depth setting

| Model EB6 Power input 1100W Voltage 230V / 50Hz, 115V / 60Hz No load r.p.m 3000~6000 Bevel angle 45 deg.(optional 30 deg.) Max. bevel height (45 deg.) 6mm Min. diameter for inside bevels 20mm Net weight 4.6 kgs (10.12Lbs) 模型eb6 电源输入功率 电压230 V / 50 Hz，115 V / 60 Hz 无负荷转速3000 ~ 6000 锥角45°（可选30°。） 最大锥高度（45°）毫米 分为内斜面直径20毫米 净重4.6公斤（10.12lbs） 标准配件 To rx扳手 钩扳手扳手 主轴锁杆 | STANDARD ACCESSORIES Torx Wrench Hook Spanner Wrench Spindle Lock Bar |
| --- | --- |

ELECTRIC / BEVELER

■The EB12 is a heavy-duty hand held beveler which uses 5 indexable carbide inserts for chatter-free beveling. The design allows straight edges, contours and cutouts to be beveled with ease. ■Works with steel, stainless steel, aluminum, copper, plastic and other materials. ■The precision dial scale allows precise adjustment of the chamfer height. ■Variable electronic feedback speed control allows stable cutting speed, no matter the load, for precision results with various materials.

| Model EB12 Power input 1800 W Voltage 230V / 50Hz , 110V / 60Hz No load r.p.m 2300-6500 Speed Wheel Settings 1/ 2/ 3/ 4/ 5/ 6: 2300/ 2600/ 3700/ 4800/ 5800/ 6500 Std. Bevel Angle 45 Deg. Max. Chamfer Height 45 Deg. : 10.6 mm Mini. Dia. For Inside Bevels 30 mm Dimensions 430mm ( L ) x 150mm (W) X 190mm (H) ( not including front handle) Net Weight 6.5kgs ( 14.3Lbs) | STANDARD ACCESSORIES Tool Holder 45 Deg. Carbide Inserts (Set of 5) Torx Wrench Hook Spanner Wrench Spindle Lock Bar Hex Wrench M6 Hard shell case |
| --- | --- |

模型eb12

输入功率1800瓦

电压230 V / 110 V / 50，60

2300-6500空载转速

车轮设置1 / 2 / 3 / 4 / 5 / 6：2300 / 2600 / 3700 / 4800 / 5800 / 6500

标准锥角45°。

最大45°倒角高度：10.6毫米

迷你。直径。内斜面30毫米

尺寸（长）×150 mm盘（宽）×离（小时）（不包括前处理）

净重量6.5kgs（14.3lbs）

标准配件

刀架45°。

硬质合金刀片（5集）

To rx扳手

钩扳手扳手

主轴锁杆

十六进制扳手，M 6

硬壳盒