室内吸顶天线（双锥）

Indoor Ceiling Antennas

| 型 号 | TQJ-800/2500-3/5 |
| --- | --- |
| 电 性 能 指 标 |
| 频率范围 VSWR 输入阻抗 增益 极化形式 最大功率 雷电防护 输入接口 | 800-960/1710-2500MHZ ≤1.4 50Ω 3/5dBi 垂直极化 50W 直流接地 N型阴头 |
| 机 械 指 标 |
| 尺寸 重量 工作温度 天线罩材料 | Φ160×143mm 0.3kg -40℃~+70℃ 防紫外线ABS |
| Model | TQJ-800/2500-3/5 |
| Electrical Specifications |
| Frequency Range VSWR Input Impedance Gain Polarization type Max power Lightning Protection Connector type | 800-960/1710-2500MHZ ≤1.4 50Ω 3/5dBi Vertical Polarization 50W DC ground N Female |
| Mechanical Specifications |
| Dimension Weight Working Temperature Radome material | Φ160×143mm 0.3kg -40℃~+70℃ UV Protected ABS |

- 安装说明：在天花板上钻一个直径为35mm的孔，

用紧固螺母将天线固定在天花板上，要求天花板

厚度不超过20mm。

- 贮藏运输：A、存贮在常温，干燥的环境中；

B、搬运过程中应轻拿轻放，防雨防潮

- 注意：天线切勿接近火源等。

- Installation  instruction: In  accordance  with   the

installation sketch, drill a hole ofΦ35mm in the ceiling.

Screw the fixing nut to fasten the antenna on the ceiling.

The ceiling’s thickness is at most 20mm.

- Storage and transportation:

  - The antenna must be stored in room temperature

and dry environment;

  - Handle the antenna with care

- Attention: The antenna mustn’t be near to fire.